Types of packets:

Packet Structure
TYPE
(RTS,CTS, INTEREST, DATA,
DEBUG[SET_LOCATION, GET_LOCATION])
SIZE (number of bytes)
SPECIFIC FRAME

Packet
Offset	Description	Size	Possible values
0	Type	1 byte	0x01 – RTS / 0x02 – CTS / 0x03 – INTEREST / 0x04 – DATA / Debug: / 0x20 – SET_INFO / 0x21 – GET_INFO_RESPONSE / 0x22 - GET_INFO_REQUEST
1	Scale	1 byte	0x00 to 0x03
2 to (n-1)	Specific Frame	Variable size
n	Checksum	1 byte	0xFF – sum(byte[0]:byte[n-1])

RTS
Offset	Description	Size	Possible values
0	Type	1 byte	0x01
1	Scale	1 byte	0x00 to 0x03
2	RTS Source Location Coordinates	Scale+1 bytes	X coordinate
2+(Scale+1)		Scale+1 bytes	Y coordinate
2+2*(Scale+1)		Scale+1 bytes	Z coordinate
2+3*(Scale+1)	Final Target Location Coordinates	Scale+1 bytes	X coordinate
2+4*(Scale+1)		Scale+1 bytes	Y coordinate
2+5*(Scale+1)		Scale+1 bytes	Z coordinate
2+6*(Scale+1)	Checksum	1 byte	0xFF – sum(byte[0]:byte[n-1])
Total size with checksum = 6*(Scale+1)+3 bytes

CTS
Offset	Description	Size	Possible values
0	Type	1 byte	0x02
1	Scale	1 byte	0x00 to 0x03
2	CTS Destination Location Coordinates	Scale+1 bytes	X coordinate
2+(Scale+1)		Scale+1 bytes	Y coordinate
2+2*(Scale+1)		Scale+1 bytes	Z coordinate
2+3*(Scale+1)	CTS Source Location Coordinates	Scale+1 bytes	X coordinate
2+4*(Scale+1)		Scale+1 bytes	Y coordinate
2+5*(Scale+1)		Scale+1 bytes	Z coordinate
2+6*(Scale+1)	Checksum	1 byte	0xFF – sum(byte[0]:byte[n-1])
Total size with checksum = 6*(Scale+1)+3 bytes

INTEREST
Offset	Description	Size	Possible values
0	Type	1 byte	0x03
1	Scale	1 byte	0x00 to 0x03
2	Next Forwarder Coordinates	Scale+1 bytes	X coordinate
2+(Scale+1)		Scale+1 bytes	Y coordinate
2+2*(Scale+1)		Scale+1 bytes	Z coordinate
2+3*(Scale+1)	Interest Region Center Coordinates	Scale+1 bytes	X coordinate
2+4*(Scale+1)		Scale+1 bytes	Y coordinate
2+5*(Scale+1)		Scale+1 bytes	Z coordinate
2+6*(Scale+1)	Interest Region Radius	Scale+1 bytes
2+7*(Scale+1)	Sink Location Coordinates	Scale+1 bytes	X coordinate
2+8*(Scale+1)		Scale+1 bytes	Y coordinate
2+9*(Scale+1)		Scale+1 bytes	Z coordinate
2+10*(Scale+1)	Variable of Interest	1 byte	0x01 - °C / 0x02 - %RH / 0x03 – ppm / …?
3+10*(Scale+1)	Precision	1 byte
4+10*(Scale+1)	Response Mode / (All respond or few respond)	1 byte	0x00 or 0x01
5+10*(Scale+1)	Interest Frequency	1 byte
6+10*(Scale+1)	Checksum	1 byte	0xFF – sum(byte[0]:byte[n-1])
Total size with checksum = 10*(Scale+1)+7 bytes

DATA
Offset	Description	Size	Possible values
0	Type	1 byte	0x04
1	Scale	1 byte	0x00 to 0x03
2	Next Forwarder Coordinates	Scale+1 bytes	X coordinate
2+(Scale+1)		Scale+1 bytes	Y coordinate
2+2*(Scale+1)		Scale+1 bytes	Z coordinate
2+3*(Scale+1)	Interest Region Center Coordinates	Scale+1 bytes	X coordinate
2+4*(Scale+1)		Scale+1 bytes	Y coordinate
2+5*(Scale+1)		Scale+1 bytes	Z coordinate
2+6*(Scale+1)	Interest Region Radius	Scale+1 bytes
2+7*(Scale+1)	Sink Location Coordinates	Scale+1 bytes	X coordinate
2+8*(Scale+1)		Scale+1 bytes	Y coordinate
2+9*(Scale+1)		Scale+1 bytes	Z coordinate
2+10*(Scale+1)	Variable of Interest	1 byte	0x01 - °C / 0x02 - %RH / 0x03 – ppm / …?
3+10*(Scale+1)	Precision	1 byte
4+10*(Scale+1)	Response Mode / (All respond or few respond)	1 byte	0x00 or 0x01
5+10*(Scale+1)	Interest Frequency	1 byte
6+10*(Scale+1)	Sensor DATA	Scale+1 bytes
6+11*(Scale+1)	Checksum	1 byte	0xFF – sum(byte[0]:byte[n-1])
Total size with checksum = 11*(Scale+1)+7 bytes

SET_INFO
Offset	Description	Size	Possible values
0	Type	1 byte	0x20
1	Scale	1 byte	0x00 to 0x03
2	Next Forwarder Coordinates	Scale+1 bytes	X coordinate
2+(Scale+1)		Scale+1 bytes	Y coordinate
2+2*(Scale+1)		Scale+1 bytes	Z coordinate
2+3*(Scale+1)	Destination Coordinates	Scale+1 bytes	X coordinate
2+4*(Scale+1)		Scale+1 bytes	Y coordinate
2+5*(Scale+1)		Scale+1 bytes	Z coordinate
2+6*(Scale+1)	New Coordinates	Scale+1 bytes	X coordinate
2+7*(Scale+1)		Scale+1 bytes	Y coordinate
2+8*(Scale+1)		Scale+1 bytes	Z coordinate
2+9*(Scale+1)	Variable	1 byte	0x01 - °C / 0x02 - %RH / 0x03 – ppm / …?
3+9*(Scale+1)	Precision	1 byte
4+9*(Scale+1)	Interest Frequency	1 byte
5+9*(Scale+1)	Checksum	1 byte	0xFF – sum(byte[0]:byte[n-1])
Total size with checksum = 9*(Scale+1)+6 bytes

GET_INFO_REQUEST
Offset	Description	Size	Possible values
0	Type	1 byte	0x22
1	Scale	1 byte	0x00 to 0x03
2	Requester Location Coordinates	Scale+1 bytes	X coordinate
2+(Scale+1)		Scale+1 bytes	Y coordinate
2+2*(Scale+1)		Scale+1 bytes	Z coordinate

GET_INFO_RESPONSE
Offset	Description	Size	Possible values
0	Type	1 byte	0x22
1	Scale	1 byte	0x00 to 0x03
2	Next Forwarder Location Coordinates	Scale+1 bytes	X coordinate
2+(Scale+1)		Scale+1 bytes	Y coordinate
2+2*(Scale+1)		Scale+1 bytes	Z coordinate
2+3*(Scale+1)	Destination Location Coordinates	Scale+1 bytes	X coordinate
2+4*(Scale+1)		Scale+1 bytes	Y coordinate
2+5*(Scale+1)		Scale+1 bytes	Z coordinate
2+6*(Scale+1)	Source Location Coordinates	Scale+1 bytes	X coordinate
2+7*(Scale+1)		Scale+1 bytes	Y coordinate
2+8*(Scale+1)		Scale+1 bytes	Z coordinate
2+9*(Scale+1)	Variable Measured	1 byte	0x01 - °C / 0x02 - %RH / 0x03 – ppm / …?
3+9*(Scale+1)	Precision	1 byte
4+9*(Scale+1)	Sampling Frequency	1 byte
5+9*(Scale+1)	Checksum	1 byte	0xFF – sum(byte[0]:byte[n-1])
Total size with checksum = 9*(Scale+1)+6 bytes

DESTINATION_LOCATION
(Immediate destination, like next hop)

RTS (FORWARDER_LOCATION, DEST_LOCATION),
CTS [](NEXTFORWARDER_LOCATION)
MESSAGE
{
INTEREST (FORWARDER_LOCATION, DESTINATION_LOCATION, SINK_LOCATION)
DATA (FORWARDER_LOCATION, SINK_LOCATION[DESTINATION], )
}